## Slide 1: EV Chips: SiC/GaN Power Semiconductors, the Supply Chain and India
Capstone 12 · AI Research Report on the Semiconductor Industry
Four AI tools (Perplexity, ChatGPT, Gemini, Claude), 39 checked sources, one verified report
Prepared by Abinaya R · October 2026

## Slide 2: EV chips and the SiC advantage
Traction inverter
SiC MOSFETs or Si IGBTs, isolated gate drivers and a real-time MCU turn battery DC into motor AC.
Battery management
Cell-monitor analog front ends, isolation ICs and an MCU track cell voltage, current and charge state.
Charger and DC-DC
GaN or SiC switches suit on-board chargers and converters; 800 V systems favour 1,200 V SiC.
>40%
lower conduction loss in a simulated SiC inverter
>60%
lower switching loss versus Si-IGBT (simulation)
>1%
higher efficiency across the torque-speed curve (simulation)
Sources: simulation study [1], TI [2], NXP [3], Power Systems Design [6]. Vendor claims reach up to 3% (ST, 2016) [8]; state the test conditions.

## Slide 3: SiC supply is concentrated in a few firms
82%
of 2024 SiC substrate revenue held by four companies
34.4%
held by two Chinese vendors, TanKeBlue and SICC
91.9%
of 2023 SiC power devices held by the top five; ST leads with 32.6%
Wolfspeed leads substrates with 33.7%; ST leads devices with 32.6%. Carmakers also need AEC-Q101 and IATF 16949 qualification, so new suppliers take time to win orders.
Sources: TrendForce [11][38]; sums and the 34.4% figure calculated by hand from the published shares.
Chart: Share of 2024 SiC substrate revenue (%) - blue = Chinese vendors
| Wolfspeed | TanKeBlue (China) | SICC (China) | Coherent | All others (derived)
Share of 2024 SiC substrate revenue (%) | 33.7 | 17.3 | 17.1 | 13.9 | 18

## Slide 4: India: 12 projects approved, a SiC fab planned
90–95%
of semiconductor demand imported (NITI Aayog)
12
ISM projects approved, about ₹1.64 lakh crore [35]
SiCSem, Bhubaneswar
First commercial SiC fab; 60,000 wafers a year; operation expected 2027–28.
Tata–PSMC, Dholera
₹91,000 crore silicon logic fab; Tata Assam packaging plant adds 48 million chips a day.
CG Power–Renesas–Stars
OSAT at Sanand for auto and industrial chips; Kaynes adds a second OSAT.
Approved is not producing: yields, qualification and customers come next. ISM 2.0 was approved in July 2026 (about ₹1.27 lakh crore).
Sources: NITI Aayog [17], PMO [14], PM India [28][35], Evertiq [32].

## Slide 5: Main risks and what the evidence says
Risk | Evidence | Caution
Import dependency | India imports 90–95% [17]; NITI scenario: US$240 billion by 2035 | Scenario, not a forecast
Oversupply | SiC revenue fell 9% in 2024; Renesas suspended SiC work | Prices volatile
Tight qualified parts | Automotive-grade wafers may fall short of announced capacity | McKinsey forecast
Geopolitics | China restricts gallium, germanium, antimony exports (Korea Times, Dec 2024) | Policy can change
Execution | Plants rely on imported equipment and materials | Approval is not output
Sources: NITI Aayog [17], TrendForce [11], Renesas [20], McKinsey [21], Korea Times [37], Global SMT [24].

## Slide 6: What we found and what AI got wrong
Findings
SiC leads EV inverters; GaN fits chargers and DC-DC.
Supply is concentrated; Chinese vendors are gaining share.
India has real approvals; imports fall only as plants qualify and ship.
AI verification
Perplexity: 9 of 20 claims fully verified.
One tool gave 1.4× more dies for 200 mm wafers; the hand check gives 1.78×.
24 errors and unsupported claims logged.
Re-check on 24 Oct 2026: 23 of 34 sources passed outright; 11 were fixed or replaced.
Lesson: ask several tools, verify every number, label scenarios and projections.